## Slide 1: Alrosa Villa/Columbus Oh. 5055 Sinclair Rd. (614) 885-2588

## Slide 2: PA System Specification
(8) High Range (4 per side) | 2” Throat JBL High Frequency Drivers
(8) Mid High Range (4 per side) | 12” JBL
(8) Mid Range (4 per side) | 15” JBL
(12) Sub Woofers (6 per side) | 18” JBL
(2) 4 Way Crossover | Brookesiren FDS360
(2) 3way Delay Speakers | Turbo Sound TMS1
(10) Power Amplifiers (5 per side) | Ashley FTX/2000
Approximately 20’000 Watts
4 Way Stereo

## Slide 3: FOH Specifications
FOH console | Mackie 40.8.2
FOH Processing (In order of Aux sends 1~4) Aux 5~8 available | (1) Lexicon PCM41 (1) Yamaha SPX900 (1) Yamaha SPX90II (1) Yamaha Rev 100
FOH Gating FOH Compression | (8) Behringer Gates (8) Behringer Compressors
FOH Drive | Ashly GQX 3102 Stereo Equalizer (1) Behringer Composer Pro

## Slide 4: Monitor World Specifications
(1) Sound Tracs MCX 32x10 Console
(8) Ashley GQX/3102 Graphic Equalizers
(2) Behringer Super X (4) 2way crossovers
(8) Ashley FTX/2000 Power Amplifiers
(1) Behringer Super X (1) 3way crossover
(1) 2 Way Brookesiren SDF-320 Crossover stereo
(1) Talk Back from FOH

## Slide 5: Monitor Specifications
ITEM/Quantity | Speaker Sizes
(6) JBL Wedges Bi Amped | (1) 15” per cab each (1) 1” High Frequency Horns per cab each
(2) Turbo Sound TXD 580 Side Fills | 15” per cab each (2) 12” x2 (1) 1’’ High Frequency Horn
(1) JBL Drum Box Tri Amped | (4) 15” (4) 12” (2) 2” Throat JBL High Frequency Horns
(3) Yamaha Wedges (Floater Mixes “Passive”) | (1) 15” per cab each (1) 1” High Frequency Horns per cab each

## Slide 6: Microphone/Accessory Selection
(2) Sure Beta 52
(1) Sure Beta 57A
(5) Sure SM 58
(3) Sure BG 4.1 condenser
(4) Senheisser 604
(1) Sure SM 57
(6) Active Direct Input Boxes
House supplies all microphone stands and cables

## Slide 7: Stage Layout
Drum Riser
Side Fill
Side Fill
PA Subs
PA
Subs
35’
21’6”
8’x 8’
Down Stage Ht. 8’7”
Up Stage Ht.10’1”
Monitor World

## Slide 8
Stage Left

## Slide 9
Center Stage

## Slide 10
Stage Right